## Slide 1
Coherence Onset and Two-Dimensional Deformation of Landfast Sea Ice at Cambridge Bay, Nunavut
Ananthanarayanan B1 and Shamjid P1,*
1 School of Digital Sciences, Digital University Kerala, Thiruvananthapuram 695317, Kerala, India
* Corresponding author: shamjid.p@duk.ac.in · ananthanarayanan.ds25@duk.ac.in
KEY MESSAGE
Free Sentinel-1 radar can date when coastal sea ice locks in place: 30 Jan in 2019, but 20 Mar in 2021 — 49 days later. The same data reproduce published ice-motion results within 2 cm.
INTRODUCTION & AIM
STUDY AREA & DATA
METHOD: FOUR STEPS, FREE DATA AND FREE CLOUD PROCESSING
RESULTS & DISCUSSION
CONCLUSIONS & NEXT STEPS
REFERENCES
Why it matters
The idea: coherence works like an ice clock
Aim: compare two contrasting winters (2018–19 vs 2020–21)
Landfast sea ice is sea ice frozen fast to the coast. Along the Canadian Arctic coast it is the winter travel surface and a key habitat. As the Arctic warms, the date it forms is shifting, so it must be measured, not assumed.
InSAR has measured the 2-D motion of this ice at Cambridge Bay [1] and its year-to-year change [2], but used coherence only to select reliable pixels. Drifting ice loses coherence and fixed ice regains it, so coherence may show when the ice consolidated and whether it stayed that way.
Coherence (0 to 1) shows how alike two radar images taken 12 days apart are, so the date it rises and stays high is the date the ice locked in place.
→
Drifting ice changes between passes → low coherence
→
Landfast ice stays in place → high coherence
Q1
When did the ice become landfast? (dated from coherence)
Q2
How did it move: east–west and up–down?
Dease Strait, Cambridge Bay, Nunavut
Sentinel-1 radar image, 17 Feb 2019
P1–P4 points on the sea ice, 1.2–8.2 km offshore
RP fixed reference on land
P5 land check point (should not move)
Green ice profiler
Sentinel-1 IW SLC data: consecutive 12-day pairs from two passes
Pass | ● Winter 2018–19 | ● Winter 2020–21
Descending (S1A, HH) | 17 Feb – 6 Apr · 4 pairs | 14 Mar – 7 Apr · 2 pairs
Ascending (S1B, VV) | 21 Feb – 17 Mar · 2 pairs | 18 Mar – 23 Apr · 3 pairs
Overlap used for 2-D motion | 21 Feb – 17 Mar (24 days) | 18 Mar – 7 Apr (20 days)
1
Make interferograms
Each 12-day pair → one interferogram, processed free in the cloud (ASF HyP3).
2
Date the lock-in
Every 12 days: share of sea ice with coherence > 0.4. Onset = first date it stays above 50%.
3
Track motion over time
SBAS time series [3], tied to fixed land (Arctic Research Station); ramps removed over stable land.
4
Split into 2-D motion
Descending looks west, ascending looks east; combining both gives east–west and up–down motion at P1–P4.
GAMMA · 20 × 4 looks (80 m) · GLO-30 DEM
Q1 · WHEN DID THE ICE LOCK IN?
In 2021 the ice locked in 49 days later than in 2019
WHAT DOES THE RAW RADAR SIGNAL SHOW? · BOTH WINTERS
Clear stripes from February in 2019, but only from mid-March in 2021
Q2 · HOW DID THE ICE MOVE? · FROM THE 8 INTERFEROGRAMS ABOVE
Offshore (P4), the ice moved west 2.7× faster and rose instead of sinking in the late winter (2020–21)
Can we trust the numbers? Within 2 cm of a published study
Chart: 12-day image pairs, mid-December to early April
| Dec |  | Jan |  |  | Feb |  | Mar |  | Apr
2018–19 | 9 | 15 | 39 | 27 | 55 | 57 | 90 | 88 | 96 | 95
2020–21 | 6 | 53 | 12 | 14 | 10 | 39 | 55 | 16 | 95 | 94
50% threshold | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
Point | This study | Chen et al. [1] | Difference
P3 | +14.8 cm | +16.7 cm | 1.9 cm
P4 | −5.6 cm | −5.4 cm | 0.2 cm
Measured before splitting into horizontal and vertical; same dates as [1] (48 days).
Precision (land point P5): ±0.7–1.6 cm.
1
Coherence resolves not only when landfast ice forms but whether formation succeeds, capturing a mid-winter break-up and refreeze invisible to deformation measurements.
2
The intermittent winter was also the more mobile, though two seasons cannot separate this from coincidence.
3
Snow metamorphism and early-growth dielectric change also cost coherence over immobile ice, so dates are late-biased; longer records and independent draft data are needed to bound this.
Coherence offers a free, repeatable way to monitor when coastal sea ice becomes landfast.
Next steps: L-band (ALOS-2) comparison, and deep-learning mapping of motion across the full Sentinel-1 archive (under way).
[1] Chen, Z., Montpetit, B., Banks, S., White, L., Behnamian, A., Duffe, J., & Pasher, J. (2021). InSAR monitoring of Arctic landfast sea ice deformation using L-band ALOS-2, C-band Radarsat-2 and Sentinel-1. Remote Sensing, 13(22), 4570. https://doi.org/10.3390/rs13224570
[2] Zhu, Y., Zhou, C., Zhu, D., Wang, T., & Zhang, T. (2023). Interannual variation of landfast ice using ascending and descending Sentinel-1 images from 2019 to 2021: A case study of Cambridge Bay. Remote Sensing, 15(5), 1296. https://doi.org/10.3390/rs15051296
[3] Berardino, P., Fornaro, G., Lanari, R., & Sansosti, E. (2002). A new algorithm for surface deformation monitoring based on small baseline differential SAR interferograms. IEEE Transactions on Geoscience and Remote Sensing, 40(11), 2375–2383. https://doi.org/10.1109/TGRS.2002.803792
https://sciforum.net/event/ECRS2026
●
2018–19 locked in on 30 Jan 2019 and stayed coherent until early April.
●
2020–21 locked in on 20 Mar 2021, 49 days later, after a break-up in early March (coherent ice 55% → 16%).
●
Only 12-day pairs work: coherence 0.78–0.81 at 12 days, but 0.54 at 24 days.
Descending pass (S1A, HH) · looks west
Ascending pass (S1B, VV) · looks east
17 Feb – 1 Mar 2019
1 – 13 Mar 2019
21 Feb – 5 Mar 2019
5 – 17 Mar 2019
14 – 26 Mar 2021
26 Mar – 7 Apr 2021
18 – 30 Mar 2021
30 Mar – 11 Apr 2021
−π
0
+π
1 colour cycle = 2.8 cm toward or away from the satellite · tight stripes = fast motion · smooth colour = little motion (e.g. land) · white = not measurable
Sideways motion (east–west, cm)
Up–down motion (cm)
2018–19
40 east
0
40 west
10 up
0
10 down
2020–21
40 east
0
40 west
20 up
0
20 down
Each map = 20 days (2019: 21 Feb – 13 Mar; 2021: 18 Mar – 7 Apr). Grey = land; white = no data; ○ P1 near shore, ◇ P4 offshore.
■ 2018–19 ■ 2020–21
Speed to the west (cm per day)
Up–down speed (cm per day)
Chart: 
| P1 (1.2 km) | P2 (2.0 km) | P3 (5.6 km) | P4 (8.2 km)
2018–19 | 0.33 | 0.56 | 0.43
2020–21 | 0.18 | 1.09 | 1.18
Chart: 
| P1 (1.2 km) | P2 (2.0 km) | P3 (5.6 km) | P4 (8.2 km)
2018–19 | 0.31 | 0.75 | -0.18
2020–21 | 0.04 | 1.05 | 1.42
n/a
n/a
n/a
n/a
2.7× faster
sinking → rising
Gaps: P2 was not measurable in 2018–19; the 2020–21 value at P3 is anomalous and left out. Per-day speeds, because the two windows differ (24 vs 20 days).
Compared: total line-of-sight motion (+ = toward the satellite), descending pass, 17 Feb – 6 Apr 2019
Acknowledgment: Copernicus Sentinel-1 data (ESA), processed with ASF HyP3 on OpenSARLab.
SESSION
S2
SAR Remote Sensing
Scan: abstract